Tender Text

Cold Water Buffer

customized design

| Pos. | Piece |  | Price |
| --- | --- | --- | --- |
|  | ……… ……… ……… | Cold water buffer storage customized design -raw- (no insulation) Cold water buffer storage for closed water systems (no oxygen supply) inside raw, outside thick primer __________ mm diameter with insulation __________ mm total height __________ l capacity Cold water inlet and outlet each 2“, thermometer connection ¾” incl. thermometer, 3 connections ¾” (e.g. for thermostats) in vessel case, connection ¾” for drainage in lower bottom with KFE tap, connection ¾” for bleeding in upper bottom. Vessel built and determined in accordance with DIN 44899, sheet 5 and worksheet W 511, suitable for 6 bar operating pressure at +95°C operating temperature, water pressure tested for 8 bar, certified An insulation which is sealed against diffusion of vapour, such as made of Armaflex plates, is not available as the vapour-sealed outer skin could be damaged during transport and during installation. We therefore suggest installing such insulation after setting up and completing the connections at the customer. Surcharge for larger water connections of flange design DN __________ (inlet and outlet) Surcharge for larger water connections of flange design DN __________ (inlet and outlet) | ……… ……… ……… |