Tender Text

Mains Water Buffer Tank with tubular desuperheater, pump and valve

- Standard -

| Pos. | Piece |  | Price |
| --- | --- | --- | --- |
|  | ……… ……… ……… ……… ……… | Service water buffer storage __________ mm diameter, no insulation __________ mm diameter, with insulation __________ mm total height __________ l capacity Walls made of 3-4.5 mm S235 JRG2, can be enamel-coated oval blank plug 100/150 mm in bottom, CW and WW each 1 ¼”, thermometer connection ¾” incl. thermometer, thermostat and circulation connection each ¾”, electric heating connection 1½”, as well as supply lines and mountings to install an external tubular desuperheater/ tubular condenser. Vessel built and determined in accordance with DIN 44899, sheet 5 and worksheet W 511, suitable for 6 bar operating pressure at +95°C operating temperature, water pressure tested for 8 bar, certified. Corrosion protection outside enamel mist, inside double enamel layer with magnesium reactive anode Insulation made of glass fibre reinforced polyester hard case with PU foam. Insulation supplied with 2 shells attached to each side of the vessel with 2 foamed-in quick acting closures. CORREX® External Current Anode -maintenance free- (alternatively to built-in serial magnesium reactive anode) electrical heater __________ kW incl. built-in thermostat Overheating protection thermostat (set to +95°C when supplied) Boiler thermostat (switching range +25/+95°C) to switch a magnetic valve in hot gas bypass line | ……… ……… ……… ……… ……… |
| Pos. | Piece |  | Price |
|  | ……… ……… | Tubular desuperheater/tubular condenser double-walled safety design comprising: Copper tube __________ mm with __________ inserted double-walled Copper finned tube 16/10 mm Length per finned tube: __________________________ m Total length of construction: ______________________ m Connection refrigerant carrying side max.: __________ mm Connection water-carrying side max.: ______________ mm Surface refrigerant carrying side: __________________ m² Water circulation volume: ________________________ m³/h Δp water: _____________________________________ bar incl. mounting incl. insulation Type Tubular desuperheater/condenser as tertiary heat exchanger built according to design D as per EN 1717, part 4, par. 5.2 temp.-depend. controlled water valve Type SW charge pump Type incl. screws, stop valve and tubular desuperheater / condenser mounted vertically to vessel. If galvanized water lines are subsequently attached to the tubular desuperheater / condenser it is necessary to nickel-plate the heat exchanger on the water carrying side. The surcharge for this is 25 %. | ……… ……… |