Tender Text

Tubular desuperheater, double-walled

with pump and valve

| Pos. | Piece |  | Price |
| --- | --- | --- | --- |
|  | ……… ……… | Tubular desuperheater/tubular condenser double-walled safety design comprising: Copper tube __________ mm with __________ inserted double-walled Copper finned tube 16/10 mm Length per finned tube: __________________________ m Total length of construction: ______________________ m Connection refrigerant carrying side max.: __________ mm Connection water-carrying side max.: ______________ mm Surface refrigerant carrying side: __________________ m² Water circulation volume: ________________________ m³/h Δp water: _____________________________________ bar incl. mounting incl. insulation Type Tubular desuperheater/condenser as tertiary heat exchanger built according to design D as per EN 1717, part 4, par. 5.2 temp.-depend. controlled water valve Type SW charge pump Type incl. screws, stop valve and tubular desuperheater / condenser mounted vertically to vessel. If galvanized water lines are subsequently attached to the tubular desuperheater / condenser it is necessary to nickel-plate the heat exchanger on the water carrying side. The surcharge for this is 25 %. | ……… ……… |