Tender Text

Water Chiller

with built-in KS-Evaporator

| Pos. | Piece |  | Price |
| --- | --- | --- | --- |
|  | ……… ……… | Cold water buffer storage for closed water system (no oxygen supply) inside raw, outside thick primer __________ mm diameter with insulation __________ mm total height __________ l capacity with connections for cold water inlet and outlet 1 ¼” or 2“ pump connection, 3 connections ¾” distributed to vessel’s jacket inc. machine thermometer –30/+50°C, switch length 160 mm installed in bottom connection of 3 connections Drainage 3/4“ with KFE tap ¾”, inc. safety valve 1“-2.5 bar, Thermometer connection 1“, inc. flange in upper vessel bottom to hold shell-&-tube evaporator. Vessel built and determined in accordance with DIN 44899, sheet 5 and worksheet W 511, suitable for 6 bar operating pressure at +95°C Operating temperature, water pressure tested for 8 bar, certified (application range up to –20°C) incl. insulation with pressure foamed design with glass fibre reinforced plastic hard case sealed against diffusion of vapour. Insulation at point of impact and connections bonded against diffusion of vapour. KS-shell-&-tube evaporator comprising: Copper shell tube __________ mm diameter with __________ inserted single-walled Cu-KS-Evaporator tubes 15 mm Length per evaporator tube: __________ m Total length: __________ m incl. __________ -fold deflection resulting in an evaporator length of __________ x __________ = __________ m, | ……… ……… |
| Pos. | Piece |  | Price |
|  | ……… ……… ……… ……… | incl. __________ -fold injection with distributor Capillary tube 5 or 6 mm, Fluid connection: __________ mm incl. suction-side conversion to __________ mm Connection water in shell: __________ inch Surface: __________ m2 Evaporator type: __________ Cold water charge pump Type: __________ Supply voltage: 230/400 V Connection dimension: for forced overflow of evaporator incl. stop valve and insulated tubes mounted to outside of vessel incl. manual and fast-action bleeder at highest point of tube Ranco switch thermostat 016-H6989 Ranco frost protection thermostat (2,0) D9040 K22-L-2564 Length of Capillary tube 2.0m with probe sleeve installed in evaporator package PS Enamelled vessel of double-walled safety evaporators can be supplied for use in the food sector. | ……… ……… ……… ……… |